| X96 Max (S905X2) |
| --- |
| CPU | Amlogic S905X2 Quad Core ARM Cortex A53 @2GHz |
| GPU | ARM Dvalin MP2 GPU |
| Memory | LPDDR4 4GB |
| Flash | eMMC 32GB(Option 64GB ) |
| WiFi | IEEE 802.11 a/b/g/n/ac 2.4G / 5.8G |
| BT | BT 4.x +HS Support Voice Remote |
| Moudle | Plastic Black Color |
| I/O | 1*HD | HD 2.1 ,Support HD CEC, Dynamic HDR and HDCP 2.2, |
|  |  | 4Kx2K@75 max resolution output. |
|  | 1*AV OUT | 480i/576i standard definition output |
|  | 2*USB | 1* USB 3.0 1*USB 2.0 |
|  | 1*IR Reciver | Remote Reciver Connect |
|  | 1*RJ45 | Ethernet Interface;Support 10/100/1000M |
|  | 1*TF CARD | Support 4GB/8GB/16GB/32GB/64GB |
| Power | DC 5V/2A LED indicator,Working Blue; |
| Software |
| OS | Android 8.1 |
| Video |  Amlogic Video Engine (AVE) with dedicated hardware decoders and encoders |
|  |  Support multi-video decoder up to 4Kx2K@60fps+1x1080P@60fps |
|  |  Supports multiple “secured” video decoding sessions and simultaneous |
|  | decoding and encoding |
|  |  Video/Picture Decoding |
|  | - VP9 Profile-2 up to 4Kx2K@60fps |
|  | - H.265 HEVC MP-10 L5.1 up to 4Kx2K@60fps |
|  | - AVS2-P2 Profile up to 4Kx2K@60fps |
|  | - H.264 AVC HP L5.1 up to 4Kx2K@30fps |
|  | - H.264 MVC up to 1080P@60fps |
|  | - MPEG-4 ASP@L5 up to 1080P@60fps (ISO-14496) |
|  | - WMV/VC-1 SP/MP/AP up to 1080P@60fps |
|  | - AVS-P16(AVS+) /AVS-P2 JiZhun Profile up to 1080P@60fps |
|  | - MPEG-2 MP/HL up to 1080P@60fps (ISO-13818) |
|  | - MPEG-1 MP/HL up to 1080P@60fps (ISO-11172) |
|  | - RealVideo 8/9/10 up to 1080P@60fps |
|  | - Multiple language and multiple format sub-title video support |
|  | - MJPEG and JPEG unlimited pixel resolution decoding (ISO/IEC-10918) |
|  | - Supports JPEG thumbnail, scaling, rotation and transition effects |
|  | - Supports *.mkv,*.wmv,*.mpg, *.mpeg, *.dat, *.avi, *.mov, *.iso, *.mp4, |
|  | *.rm and *.jpg file formats |
| Audio | Supports MP3, AAC, WMA, RM, FLAC, Ogg and programmable with 7.1/5.1 down-mixing |
|  | Built-in serial digital audio SPDIF/IEC958 input/output and PCM input/output built-in TDM/PCM/I2S ports with TDM/PCM mode up to 384kHz x32bits x 8ch or |
|  | 96kHz x 32bits x 32ch and I2S mode up to 384kHz x 32bits x 8ch |
|  | Digital microphone PDM input with programmable CIC, LPF & HPF, support up to 8 DMICs |
|  | Built-in stereo audio DAC |
|  | Supports concurrent dual audio stereo channel output with combination |
|  | of analog+PCM or I2S+PCM |
| Image | HD JPEG,BMP,GIF,PNG,TIF |
| Language | English French German Spanish Italian etc multilateral languages |
| Appliactions |
| Online | Browse all video websites,support Netflix,Hulu,Flixster, Youtube, etc. |
| Apps | Apps download freely form android market,amazon app store etc. |
| Medium | Local Media playback,Support HDD, U Disck ,TF Card . |
| Talk online | Support SKYPE video call ,MSN , facebook ,twitter ,QQ etc |
| Others | Support Email,office suit etc. |
|  | Support DLNA function |
|  | Support 2.4G wireless mouse/keyboard |
| Accessories |
| 1,HD cable *1 |
| 2,IR Remote *1 |
| 3,User Manual *1 |
| 4,Package box *1 |
| 5,Power adapter *1 |