## Slide 1: AH Redundant System
Ethan
PLCBU
MAR, 2018

## Slide 2: Forms of Redundant System
Parallel Redundant System
Voting Redundant System
Double 2-vote-2 Redundancy (D2V2R)
A1
A2
A3
An
…
Input
Output
Main System
Redundant
System
Redundant
System
Redundant
System
A1
A2
A3
An
…
Input
n/k
Voter
Output
Input
A1
A2
B1
B2
Voter
Output
Voter
Main System
Redundant System
Rock Well：1756 L6X/L7X
Mitsubishi：Q12/Q25PRHCPU
Siemens：S7-400
Delta：AHCPU560-EN2
Schneider：M580
OMRON：CS1D
Functional Safety SIL3
Functional Safety SIL4
Notes: 冗余系統架構可以分成三種 並聯 表決 跟 複合型
並聯系統是由多組控制系統所組成 當主控制系統發生異常時 則會由冗余控制系統接替
今天所要介紹的 AH冗余主機 就是屬於這種類型
表決系統則是透過表決器 來決定輸出為何 表決器 則是透過硬體電路的設計 或是 程式邏輯的方式來實現
2乘2取2系統其實就是結合並聯與表決系統所構成

## Slide 3: Types of Redundancy
Power Redundancy
CPU Redundancy
Communication Redundancy
Cable Redundancy
I/O Redundancy
AH500
Redundant
System
(Stage 1)
AH500 Redundant System
(Stage 2)
Notes: AH冗余主機的冗余功能開發的分成兩個階段
第一階段包含了電源 主機 通訊與線路冗余 四種
在稍後會逐項跟大家進行介紹
而I/O冗余則會在第二階段進行開發

## Slide 4: AH560-EN2 Introduction
SD Card Type
Micro SD (max 32GB)
Network COM Port
RJ45 x2
EtherNet/IP (DLR)
Serial Communication Port
European-style terminal block
RS232/RS485
Fiber Optics Module
Data synchronization
1. LCP-155A4HDRJ
2. LCP-155B4JDRJ
3. LCP-155B4MDRJ
AH560-EN2
Types of Redundancy
AH560_EN CPU
Redundant Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Specifications
AH Series Selection

## Slide 5: AH560-EN2 Introduction
Power Redundancy
AHPS05-5A
AHPS15-5A
Redundancy of Extension Backplanes ：AHBP06ER1-5A、AHBP08ER1-5A
Redundant Main Backplane：AHBP04MR1-5A
AH560-EN2
Types of Redundancy
AH560_EN CPU
Redundant Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Specifications
AH Series Selection

## Slide 6: AH560-EN2 Introduction
Communication Redundancy in Extension Backplanes
Redundancy of Extension Backplanes ：AHBP06ER1-5A、AHBP08ER1-5A
Redundant Main Backplane：AHBP04MR1-5A
AH560-EN2
Types of Redundancy
AH560_EN CPU
Redundant Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Specifications
AH Series Selection

## Slide 7: AH560-EN2 Introduction
Item | AHCPU560-EN2
Execution | The program is executed cyclically
I/O Control | Regenerated inputs/outputs Direct inputs/outputs
Programming language | IEC 61131-3
 | Ladder、FBD、IL、ST、SFC
Instruction execution speed | 12K Steps/ms
Number of Instructions | 666 instructions
Constant scan cycle (ms) | 1-32000 (The scan cycle can be increased by one millisecond)
Program capacity | 1M Steps
Installation | DIN rails or screws
Installation of a module | A module is installed directly on a backplane
Connection between two Backplanes | An extension cable connects two backplanes
Max. installed modules | 64 modules
Max. connected backplanes | 8 backplanes
Number of tasks | Single Mode: 283 tasks (32 cyclic tasks; 32 I/O interrupts; 4 timed interrupts; 2 communication interrupts; 1 external 24 V low-voltage; interrupt; 212 external interrupts) Redundant Mode: 36 tasks (32cyclic; tasks; 4 timed interrupts)
Numbers of I/O | Single Mode: 4352 points Redundant Mode: 3584 points
Input relays [X] | 65536（X0.0~X4095.15）
Output relays [Y] | 65536（Y0.0~Y4095.15）
Internal relays [M] | 8192（M0~M8191）
Link registers [L] | 262144（L0~262143）
Item | AHCPU560-EN2
Timers [T] | 2048（T0~T2047）
Counters [C] | 2048（C0~C2047）
32-bit counter [HC] | 64（HC0~HC63）
Data register [D] | 262144（D0~D262143）
Stepping relay [S] | 4096（S0~S4095）
Index register [E] | 32（E0~E31）
Special auxiliary relay[SM] | 4096 ( SM0~SM4095 )
Special data register [SR] | 4096 ( SR0~SR4095 )
Serial communication port | One RS-232/485
Ethernet Port | 10/100M
Modbus TCP Connections (Slave) | 32
Modbus TCP Connections (Master) | 128
EtherNet/IP CIP Connections | 256 (Slave+Master)
EtherNet/IP TCP Connections | 128 (Slave+Master)
USB Port | Mini USB
Storage interface | Micro SD
Remote RUN/STOP | The setting range is X0.0~X511.15
Real-time clock | Years, months, days, hours, minutes, seconds, and weeks
Switched Time | 20ms
Synchronous Speed | 0.5 ms/kbyte
AH560-EN2
Types of Redundancy
AH560_EN CPU
Redundant Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Specifications
AH Series Selection

## Slide 8: AH560-EN2 Introduction
Backplane Lists |  | AH5x0 AH5x1 | AH560 (Single Mode) | AH560 (Redundant Mode)
Main Backplanes | AHBP04M1-5A | ○ | ○ | ○
 | AHBP06M1-5A | ○ | ○ | ○
 | AHBP08M1-5A | ○ | ○ | ○
 | AHBP12M1-5A | ○ | ○ | ○
Extension Backplanes | AHBP06E1-5A | ○ | ○ | ×
 | AHBP08E1-5A | ○ | ○ | ×
Redundant Main Backplane (*1) | AHBP04MRI-5A | ○ | ○ | ○
Redundancy of Extension Backplanes (*1) | AHBP06ERI-5A | ○ | ○ | ○
 | AHBP08ERI-5A | ○ | ○ | ○
*1：Power Redundancy *2：Extension Backplanes can’t work with Redundancy of Extension Backplanes at the same time |  |  |  | 
AH560-EN2
Types of Redundancy
AH560_EN CPU
Redundant Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Specifications
AH Series Selection

## Slide 9: Redundant Architecture
9
Standby CPU
Master CPU

AH560-EN2
Types of Redundancy
AH Redundant System
Extension Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Circuit Redundancy
Network Redundancy
. SYNC Cable (Fiber Optics)

## Slide 10: Redundant Architecture
10
Redundancy of Extension Backplane

Standby CPU
Master CPU
Redundancy of Extension Backplane

AH560-EN2
Types of Redundancy
AH Redundant System
Extension Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Circuit Redundancy
Network Redundancy
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane

## Slide 11: Redundant Architecture
RTU
11
Redundancy of Extension Backplane

Standby CPU
Master CPU
Redundancy of Extension Backplane

RTU

AH560-EN2
Types of Redundancy
AH Redundant System
Extension Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Circuit Redundancy
Network Redundancy
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane
. Ring Network ( DLR )
EtherNet/IP

## Slide 12: Redundant Architecture

Workstation
12

Standby CPU
Master CPU
Redundancy of Extension Backplane

RTU

RTU
Ring Redundancy
AH560-EN2
Types of Redundancy
AH Redundant System
Extension Backplane
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Circuit Redundancy
Network Redundancy
Redundancy of Extension Backplane
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane
. Ring Network ( DLR )
EtherNet/IP
. Star Network
EtherNet/IP
Modbus TCP

## Slide 13: Types of Redundancy

Master CPU

RTU
Redundancy of Extension Backplane

Standby CPU
Redundancy of Extension Backplane

RTU

13
AH560-EN2
Types of Redundancy
Power Redundancy
CPU Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Communication Redundancy in Extension Backplanes
Network Redundancy
Ring Redundancy
Workstation
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane
. Ring Network ( DLR )
EtherNet/IP
. Star Network
EtherNet/IP
Modbus TCP
Notes: Power redundant (1)

## Slide 14: Types of Redundancy

RTU
14
Redundancy of Extension Backplane

Standby CPU
Master CPU
Redundancy of Extension Backplane

RTU

Ring Redundancy
Workstation
AH560-EN2
Types of Redundancy
Power Redundancy
CPU Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Communication Redundancy in Extension Backplanes
Network Redundancy
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane
. Ring Network ( DLR )
EtherNet/IP
. Star Network
EtherNet/IP
Modbus TCP
Notes: CPU redundant (1)

## Slide 15: Types of Redundancy

RTU
15
Redundancy of Extension Backplane


Master CPU
Standby CPU
Redundancy of Extension Backplane

RTU


Workstation
Ring Redundancy
AH560-EN2
Types of Redundancy
Power Redundancy
CPU Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Communication Redundancy in Extension Backplanes
Network Redundancy
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane
. Ring Network ( DLR )
EtherNet/IP
. Star Network
EtherNet/IP
Modbus TCP
Notes: CPU redundant (1)

## Slide 16: Types of Redundancy

RTU
16
Redundancy of Extension Backplane

Standby CPU
Master CPU
Redundancy of Extension Backplane

RTU


Workstation
Ring Redundancy
AH560-EN2
Types of Redundancy
Power Redundancy
CPU Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Communication Redundancy in Extension Backplanes
Network Redundancy
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane
. Ring Network ( DLR )
EtherNet/IP
. Star Network
EtherNet/IP
Modbus TCP
Notes: CPU redundant (1)

## Slide 17: Types of Redundancy

RTU
RTU
17
Redundancy of Extension Backplane

Standby CPU
Master CPU
Redundancy of Extension Backplane



Workstation
Ring Redundancy
AH560-EN2
Types of Redundancy
Power Redundancy
CPU Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Communication Redundancy in Extension Backplanes
Network Redundancy
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane
. Ring Network ( DLR )
EtherNet/IP
. Star Network
EtherNet/IP
Modbus TCP
Notes: CPU redundant (1)

## Slide 18: Types of Redundancy

RTU
18
Redundancy of Extension Backplane

Master CPU
Standby CPU
Redundancy of Extension Backplane

RTU


Workstation
Ring Redundancy
AH560-EN2
Types of Redundancy
Power Redundancy
CPU Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Communication Redundancy in Extension Backplanes
Network Redundancy
. SYNC Cable (Fiber Optics)
. Extension Cable for
connecting extension
backplane
. Ring Network ( DLR )
EtherNet/IP
. Star Network
EtherNet/IP
Modbus TCP
Notes: CPU redundant (1)

## Slide 19: Redundant Configuration
Selection of Extension Backplane：
AHBP06ER1-5A
AHBP08ER1-5A
Modules Selection for Main Backplane：
AH10SCM-5A v1.06 or later version
AH15SCM-5A v1.02 or later version
AH10EN-5A v2.04 or later version
AH15EN-5A
Modules Selection for Extension Backplane：
Digital I/O Module
Analog I/O Module
AH10SCM-5A (v1.06)
AH15SCM-5A (v1.02)
Tasks Limitation：
Cyclic tasks
Timed tasks
Supported Software Versions：
ISPSoft 3.04 or later version
DCISoft 1.19 or later version
EIP Builder 1.05 or later version
System Limitation
Check
Enable Redundancy
Determine Conditions
Data Synchronization
Synchronous Data Capacity
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice

## Slide 20: Redundant Configuration
ISPSoft -> HWCONFIG -> CPU -> System
System Limitation
Check
Enable Redundancy
Determine Conditions
Data Synchronization
Synchronous Data Capacity
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice

## Slide 21: Redundant Configuration
Master CPU
Standby CPU
Whether Enable Redundant Mode?
The order for powering on CPU Master CPU is the first one to power on
Whether CPU have projects?
Whether CPU have errors?
CPU MAC value Master CPU MAC value is the largest
192.168.1.1
192.168.1.13
192.168.1.15
192.168.1.17
192.168.1.14
192.168.1.2
SYNC Cable (Fiber Optics)
System Limitation
Check
Enable Redundancy
Determine Conditions
Data Synchronization
Synchronous Data Capacity
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice

## Slide 22: Redundant Configuration
Master CPU
CPU FW versions must be compatible
Module selections must be the same
CPU and its according communication modules must at the same physical domain
Unsynchronized
Synchronize



Notice：Compatibility of FW version is according to sub-version value of digital in tens, like 1.0X.X compatible with 1.00.0
System Limitation
Check
Enable Redundancy
Determine Conditions
Data Synchronization
Synchronous Data Capacity
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
SYNC Cable (Fiber Optics)

## Slide 23: Redundant Configuration
First time synchronization：
CPU Project
CPU Setting Value
Module Setting
Real-Time Clock
Cyclic Synchronization：
Changed Devices
Stop/Run LED status indicator
The parameters in the CPU modules
Synchronize
Synchronizing Time：
The end of scan
Synchronization points of tasks
Timed interrupt tasks
System Limitation
Check
Enable Redundancy
Determine Conditions
Data Synchronization
Synchronous Data Capacity
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable (Fiber Optics)

## Slide 24: Redundant Configuration
Device Change：
D0、D1000
M0
Device Change：
D0、D1、D2、D1000
M0、M1、M2
Synchronous Data Capacity：
=> 1536 Words
Synchronous Data Capacity：
=> 1536 Words
Every 512 words as one range
System Limitation
Check
Enable Redundancy
Determine Conditions
Data Synchronization
Synchronous Data Capacity
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable (Fiber Optics)

## Slide 25: System Switch
Standby CPU
Master CPU
192.168.1.1
192.168.1.14
192.168.1.2
192.168.1.13
The scenarios to cause system switch：
Errors in AH CPU(including of errors in the modules)
Add or remove modules
Removal of connection cable from CPU or communication modules
Instruction of system switch
Switching Conditions
Program Execution
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
SYNC Cable (Fiber Optics)

## Slide 26: System Switch
Master CPU
Standby CPU
192.168.1.1
192.168.1.14
192.168.1.2
192.168.1.13
192.168.1.13
192.168.1.1
192.168.1.14
192.168.1.2
Switching Conditions
Program Execution
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
The scenarios to cause system switch：
Errors in AH CPU(including of errors in the modules)
Add or remove modules
Removal of connection cable from CPU or communication modules
Instruction of system switch
SYNC Cable (Fiber Optics)

## Slide 27: System Switch
Standby CPU
Master CPU
System Switch
Synchronizing Time：
Synchronization points of tasks
Timer interrupt tasks
The end of scan
Task1
Task2
Task3
Task4
Task5
END
Task1
Task2
Task3
Task4
Task5
END
Switching Conditions
Program Execution
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
SYNC Cable (Fiber Optics)
Task executing orders

## Slide 28: System Switch
System Switch
Synchronizing Time：
Synchronization points of tasks
Timer interrupt tasks
The end of scan
Task1
Task2
Task3
Task4
Task5
END
Task3
Task4
Task5
END
Synchronizing Time：
Synchronization points of tasks
Timer interrupt tasks
The end of scan
Switching Conditions
Program Execution
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable (Fiber Optics)
Task executing orders

## Slide 29: System Switch
Synchronizing Time：
Synchronization points of tasks
Timer interrupt tasks
The end of scan
Task executing orders
Task3
Task3
Timer
Task
Task1
Task2
Task3
Task4
System Switch
END
Task4
END
…
Switching Conditions
Program Execution
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable (Fiber Optics)

## Slide 30: System Switch
Task3
Task3
…
Synchronizing Time：
Synchronization points of tasks
Timer interrupt tasks
The end of scan
Task3
System Switch
Task3
Task4
END
…
Switching Conditions
Program Execution
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable (Fiber Optics)
Task executing orders
Task1
Task2
Task4
END
Timer
Task

## Slide 31: Software Operation
SSO：System Switch
RCS：Redundant System Info
0：CPU ID
1：Redundant System Status
2：Power Modules Status
3：Master/Standby CPU LED Status
S Description
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 32: Software Operation
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 33: Software Operation
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 34: Software Operation
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 35: Software Operation
Standby CPU
Master CPU
SYNC Cable
(Fiber-Optics)
CPU ID ：A
CPU ID ：B
Change Master CPU to B
CPU ID：B
Change Standby CPU to A by itself
CPU ID ：A
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 36: Software Operation
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Setting of Synchronous | Allow Communication | Initiate Qualification check | Qualification check | Synchronous Data | Cyclic Check
Always | 1. Master CPU | Automatic | 1. Controller FW version 2. Main backplane module configurations 3. Same network | 1. Controller projects 2. Controller module configurations 3. Controller device values | 1. Any serious errors in the system 2. Bus fault 3. Same physical domain 4. Standby CPUs exist or not
Conditions | 1. Master CPU 2. Standby CPU | Manual | 1. Controller FW versions | 1. Controller device values | 1. Any serious errors in the system 2. Standby CPUs exist or not
RTU Setting
(EIP DLR)

## Slide 37: Software Operation
Unsynchronized
Synchronize
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable
(Fiber-Optics)
RTU Setting
(EIP DLR)

## Slide 38: Software Operation
Unsynchronized
Synchronize
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable
(Fiber-Optics)
RTU Setting
(EIP DLR)

## Slide 39: Software Operation
Synchronize
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable
(Fiber-Optics)
RTU Setting
(EIP DLR)

## Slide 40: Software Operation
The functional button only works without Master CPU existing
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Standby CPU
Master CPU
SYNC Cable
(Fiber-Optics)
RTU Setting
(EIP DLR)

## Slide 41: Software Operation
Current synchronous data capacity：
SR24~SR25
The largest of historic synchronous data capacity：
SR26~SR27
Currently connected controllers：
Master CPU
Standby CPU
Current system status：
Redundant system is checking
Redundant system is ready
Single Mode
Failure of redundant system
SYNC cable is not connected
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 42: Software Operation
1. Click EIP Builder
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 43: Software Operation
2. Communication Setting
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 44: Software Operation
3. Scan Network
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 45: Software Operation
4. Click the right button for Fast Connect
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 46: Software Operation
5. RTU Module Setup
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 47: Software Operation
6. Downloader
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)
RTU parameters
PLC data exchange table

## Slide 48: Software Operation
7. On-line Mode
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 49: Software Operation
8. Enable DLR
5
3
4
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 50: Software Operation
9. Error Detection
Redundant System API Instructions
System Error Log
Redundant System Event Records
Redundant System Info.
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
RTU Setting
(EIP DLR)

## Slide 51: Practice
Starting Kits
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice

## Slide 52: Practice
System Switch
Starting Kits
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice

## Slide 53: Practice
Power Switch
Starting Kits
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice

## Slide 54: Practice
Ring Network
HMI
RTU
Ring Network
EtherNet/IP DLR
Start Network
Switch
Master CPU
Standby CPU
Starting Kits
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice

## Slide 55: Practice
Start Network
HMI
Master CPU
Standby CPU
RTU
Ring Network
EtherNet/IP DLR
Start Network
Starting Kits
AH560-EN2
Types of Redundancy
Redundant Configuration
System Switch
Software Operation
Redundant Architecture
Practice
Switch

## Slide 56: Q&A